## Slide 1: Drawing Lines and Working with Layers
Drawing Lines
Drawing with Coordinates
Drawing with Polar Tracking
Drawing with Layers

## Slide 2: Drawing Lines
Draw a line by selecting points on-screen.
Create a closed shape with the line command.
Undo individual line segments.
Draw a line that continues from a previous line endpoint.
Objectives:

## Slide 3: Drawing Lines
Ribbon: Home  Draw  Line

## Slide 4: Creating a Closed Shape
After creating at least two line segments, it is possible to close the shape by selecting the [Close] option in the Command line.

## Slide 5: Undo a Line Segment
While drawing lines, a mistake may occur. To delete the last line segment drawn, select the [Undo] option in the Command line.

## Slide 6: Exercise: Drawing Lines
2.1.1 Drawing Lines

## Slide 7: Drawing with Cartesian Coordinates
Draw a precise line by entering absolute coordinate values.
Draw a precise line by entering relative coordinate values.
Draw a precise line by entering polar coordinate values.
Objectives:

## Slide 8: Drawing Lines Using Absolute Coordinates
Any time AutoCAD prompts you to specify a point, such as in the line command, you can type in an absolute coordinate value in the format: X,Y.

## Slide 9: Drawing Lines Using Relative Coordinates
Any time AutoCAD prompts you to specify a point, such as in the Line command, you can type in an relative coordinate value in the format: @X,Y.
The line is drawn relative to the last point, rather than the drawing origin.

## Slide 10: Drawing Lines Using Polar Coordinates
Any time AutoCAD prompts you to specify a point, such as in the Line command, you can type in a polar coordinate value in the format: @Length<Angle.

## Slide 11: Exercises: Drawing with Cartesian Coordinate Methods
2.2.1 Drawing a Rectangle with Absolute Coordinates
2.2.2 Drawing a More Complex Shape with Absolute Coordinates
2.2.3 Drawing a Rectangle with Relative Coordinates
2.2.4 Drawing a More Complex Shape with Relative Coordinates
2.2.5 Drawing a Rectangle with Polar Coordinates
2.2.6 Drawing a More Complex Shape with Polar Coordinates

## Slide 12: Drawing with Polar Tracking
Use Direct Distance Entry to draw lines of specific length.
Use ORTHO to draw horizontal and vertical lines.
Use Polar Tracking to draw lines at specified angles.
Set Incremental and Additional Angles in the Polar Tracking settings.
Objectives:

## Slide 13: Direct Distance Entry
Typically, the fastest way to draw a line is through direct distance entry. This occurs by picking the initial point, moving the crosshairs in the direction you wish to draw, then typing in the length of the line.
While it is a fast method of drawing a line at a given length, Direct Distance Entry alone does not control the angle at which the line is drawn.
To be used effectively Direct Distance Entry must be used in conjunction with another tool such as Orthogonal Locking (ORTHO) or Polar Tracking.

## Slide 14: Orthogonal Locking (ORTHO)
The ORTHO mode can be enabled by selecting the appropriate button on the status bar.
The ORTHO mode allows for the easy creation of horizontal and vertical lines.

## Slide 15: Polar Tracking
Polar Tracking can be enabled by selecting the appropriate button on the status bar.

## Slide 16: Increment Tracking Angles
Clicking the fly-out arrow next to the Polar Tracking button will display commonly used increment angles.
An increment angle will allow your mouse to snap on every increment of that angle from 0 to 360 degrees.

## Slide 17: Additional Tracking Angles
Occasionally you will need to draw at additional specified angles without the need for increments.
For example, you may need to draw a line that is 4 units long at a 50 degree angle. You do not, however, need to draw at each increment of 50 (50, 100, 150, etc.).
To add an additional angle, click the fly-out arrow next to the Polar Tracking status bar button, then select Tracking Settings…

## Slide 18: Additional Tracking Angles
Click <<New>>, type in the desired additional angle, then press [Enter] at the keyboard.

## Slide 19: Exercises: Drawing with Polar Tracking
2.3.1 Drawing a Rectangle with Polar Tracking
2.3.2 Drawing a More Complex Shape with Polar Tracking
2.3.3 Drawing with Additional Polar Tracking Angles
2.3.4 Drawing with Architectural Units
2.3.5 Polar Tracking Challenge Exercise

## Slide 20: Drawing with Layers
Draw objects in specific layers.
Change the layer of existing objects.
Turn layers on and off.
Freeze and thaw layers.
Lock layers.
Create new layers.
Objectives:

## Slide 21: Setting the Current Layer
The Layer Control is located at Ribbon: Home  Layers.
Whichever layer is visible on the Layer Control is known as the Current Layer. This means that any object that is drawn will be created on that particular layer.
The current layer can be changed by selecting the drop-down arrow and then selecting the name of the layer that you would like to use.

## Slide 22: Changing the Layer of Existing Objects
Select the objects while no command is active, then click the drop-down arrow on the Layer Control and select the desired layer.
Press [Esc] at the keyboard to deselect the objects.

## Slide 23: Turning Layers On and Off
Turning a layer off will result in all objects on that layer becoming invisible.
To turn a layer on or off click the drop-down on the layer control, then click the light bulb next to the name.

## Slide 24: Freezing and Thawing Layers
Freezing a layer will result in all objects on that layer becoming invisible.
To freeze or thaw a layer click the drop-down on the layer control, then click the sun or snowflake next to the name.

## Slide 25: Locking and Unlocking Layers
Locking a layer will prevent all objects on that layer from being modified.
To lock or unlock a layer click the drop-down on the layer control, then click the padlock next to the name.

## Slide 26: Layer Properties Manager
The Layer Properties Manager is where you will create and modify layers.
It is located at Ribbon: Home  Layers  Layer Properties.

## Slide 27: Creating a New Layer
Select the New Layer button.
Rename the layer.
Specify a color for the layer.
Specify a linetype for the layer.
Specify a lineweight for the layer.

## Slide 28: Exercises: Drawing with Layers and Adjusting Layer Settings
2.4.1 Drawing with Layers
2.4.2 Changing the Layers of Existing Objects
2.4.3 Modifying Layer States
2.4.4 Creating and Modifying Layers
2.4.5 Layers Challenge Exercise