## Slide 1: Drawing Additional Objects (Part I)
Drawing Circles
Drawing Rectangles
Drawing Polygons

## Slide 2: Drawing Circles
Draw a circle using the Center, Radius method.
Draw a circle using the Center, Diameter method.
Draw a circle using the 2-Point method.
Draw a circle using the 3-Point method.
Draw a circle using the Tan, Tan, Radius method.
Draw a circle using the Tan, Tan, Tan method.
Objectives:

## Slide 3: Drawing Circles
Ribbon: Home  Draw  Circle
The default circle command option is Center, Radius. Select the drop-down button to access several other methods for drawing circles.

## Slide 4: Drawing a Circle Using the Center, Radius Method
Select the Circle command drop-down (if necessary), then select the Center, Radius option.
Specify the center of the circle by typing a coordinate value or by selecting a location on-screen.
Specify the radius value by typing a value or selecting a location on-screen.

## Slide 5: Drawing a Circle Using the Center, Diameter Method
Select the Circle command drop-down (if necessary), then select the Center, Diameter option.
Specify the center of the circle by typing a coordinate value or by selecting a location on-screen.
Specify the diameter value by typing a value or selecting a location on-screen.

## Slide 6: Drawing a Circle Using the 2-Point Method
Select the Circle command drop-down, then select the 2-Point option.
Specify one point on the circumference of the circle by typing a coordinate value or by selecting a location on-screen.
Specify the point on the opposite side of the circle by typing a value or by selecting a location on-screen.

## Slide 7: Drawing a Circle Using the 3-Point Method
Select the Circle command drop-down (if necessary), then select the 3-Point option.
Specify one point on the circumference of the circle by typing a coordinate value or by selecting a location on-screen.
Specify a second point on the circumference of the circle by typing a coordinate value or by selecting a location on-screen.
Specify a third point on the circumference of the circle by typing a coordinate value or by selecting a location on-screen.

## Slide 8: Drawing a Circle Using the Tan, Tan, Radius Method
Select the Circle command drop-down (if necessary), then select the Tan, Tan, Radius option.
Select the first object (line, arc, circle, etc.) that the created circle needs to be tangent to.
Select the second object that the created circle needs to be tangent to.
Type the radius of the circle.

## Slide 9: Drawing a Circle Using the Tan, Tan, Tan Method
Select the Circle command drop-down (if necessary), then select the Tan, Tan, Tan option.
Select the first object (line, arc, circle, etc.) that the circle needs to be tangent to.
Select the second object that the circle needs to be tangent to.
Select the third object that the circle needs to be tangent to.

## Slide 10: Exercises: Drawing Circles
3.1.1 Drawing Circles with the Center, Radius and Center, Diameter Methods
3.1.2 Additional Practice with the Center, Radius and Center, Diameter Methods
3.1.3 Drawing Circles with the 2-Point and 3-Point Methods
3.1.4 Drawing Circles with Tangent Methods
3.1.5 Drawing Circles Challenge Exercise

## Slide 11: Drawing Rectangles
Draw a rectangle by picking points.
Draw a rectangle using relative coordinates.
Objectives:

## Slide 12: Drawing Rectangles
Ribbon: Home  Draw  Rectangle
To draw a rectangle you must specify two diagonal end points.
The first point can be placed by picking a point on-screen, or typing a coordinate value.
The second point can be placed by typing in relative coordinates.

## Slide 13: Exercises: Drawing Rectangles
3.2.1 Drawing Rectangles
3.2.2 Drawing Rectangles Challenge Exercise

## Slide 14: Drawing Polygons
Draw a polygon using the Inscribed method.
Draw a polygon using the Circumscribed method.
Draw a polygon using the Edge method.
Objectives:

## Slide 15: Drawing Polygons
Ribbon: Home  Draw  Polygon
The first time the Polygon command is used, you will need to click the drop-down arrow next to the Rectangle command to access the Polygon command.

## Slide 16: Drawing a Polygon with the Inscribed Option
The Inscribed option is the preferred method when you know the distance from the center of the polygon to each of its points.
Start the Polygon command.
Specify the number of sides.
Specify the center of the polygon.
Select the Inscribed option.
Specify the radius of the guide circle.

## Slide 17: Drawing a Polygon with the Circumscribed Option
The Circumscribed option is the preferred method when you know the distance from the center of the polygon to each of its flat surfaces.
Start the Polygon command.
Specify the number of sides.
Specify the center of the polygon.
Select the Circumscribed option.
Specify the radius of the guide circle.

## Slide 18: Drawing a Polygon with the Edge Option
The Edge option is the preferred method when you know the length of each of the flat surfaces.
Start the Polygon command.
Specify the number of sides.
Select the Edge option.
Specify a start point.
Using Polar Tracking, specify a length and direction for the first edge.

## Slide 19: Exercises: Drawing Regular Polygons
3.3.1 Drawing Polygons
3.3.2 Additional Practice Drawing Polygons
3.3.3 Drawing Polygons Challenge Exercise