## Slide 1: Object Snaps and Object Snap Tracking
Drawing with Object Snaps
Drawing with Object Snap Tracking

## Slide 2: Drawing with Object Snaps
Draw new objects while snapping to geometric components of existing objects, including:
  Endpoint
  Midpoint
  Center Point
  Geometric Center
  Node
  Quadrant
  Intersection
  Insertion Point
  Perpendicular
  Tangent
  Nearest
Objectives:

## Slide 3: Running Object Snaps
Status Bar: Object Snap

## Slide 4: Running Object Snaps
Clicking the drop-down arrow next to the OSNAP icon will bring up the menu of Object Snaps
This method of using Object Snaps is known as Running mode because the selected Object Snaps are always on, unless an override is applied.

## Slide 5: Running Object Snaps
While in a drawing command, hover the crosshairs over an object.
An autosnap marker will appear, indicating that AutoCAD will snap to that geometric location.
Simply click to draw at that location.

## Slide 6: Object Snap Overrides
Snaps that are used occasionally will work better as overrides, rather than running object snaps
Hold [Shift] at the keyboard while simultaneously right-clicking the mouse
The Object Snap Override menu appears
Select the desired object snap
The object snap is only available for one click

## Slide 7: Exercises: Drawing with Object Snaps
4.1.1 Drawing with Endpoint, Midpoint, and Quadrant Object Snaps
4.1.2 Drawing with Center and Tangent Object Snaps
4.1.3 Drawing with Node and Perpendicular Object Snaps
4.1.4 Drawing with Intersection and Geometric Center Object Snaps
4.1.5 Drawing with Object Snap Overrides
4.1.6 Additional Practice Drawing with Object Snap Overrides
4.1.7 Object Snaps Challenge Exercise #1
4.1.8 Object Snaps Challenge Exercise #2

## Slide 8: Drawing with Object Snap Tracking
Track off of existing drawing objects to locate points
Draw with the Parallel Object Snap
Draw with the Extension Object Snap
Objectives:

## Slide 9: Object Snap Tracking
Status Bar: Object Snap Tracking
OTRACK will allow you to track off of Object Snap locations such as endpoint, center, midpoint, etc.
Therefore, in addition to enabling OTRACK, OSNAP must also be enabled

## Slide 10: Object Snap Tracking
Hover the crosshairs over a point to acquire it
After a point is acquired, you will see a tracking line appear when the crosshair is moved horizontally or vertically away from that point.

## Slide 11: Extension Snap
The Extension snap will allow you to track off of the endpoint of an existing line
Rather than track orthogonally, however, it will track the same vector as the line
The Extension snap also allows for tracking off of the endpoint of an arc

## Slide 12: Parallel Snap
The Parallel snap will allow you to track off of an existing line in order to create a line parallel to it
The first endpoint of the new line must first be selected.
Then, hover the crosshairs over the line that you wish to be parallel to
A tracking point appears

## Slide 13: Parallel Snap
Finally, move the crosshairs back to the new line location and a tracking line appears at the parallel location
Select a point or type a length to create the parallel line

## Slide 14: Exercises: Drawing with Object Snap Tracking
4.2.1 Tracking Off of a Single Point with Object Snap Tracking
4.2.2 Object Snap Tracking of Multiple Points
4.2.3 Object Snap Tracking Challenge Exercise