## Slide 1: Modifying Drawing Objects
Moving Drawing Objects
Scaling Drawing Objects
Stretching Drawing Objects
Rotating Drawing Objects
Trimming Drawing Objects
Extending Drawing Objects
Creating Rounded Corners with the Fillet Command
Creating Angled Corners with the Chamfer Command

## Slide 2: Moving Drawing Objects
Move an object by entering a distance value
Move an object to a new location by snapping to existing drawing objects
Objectives:

## Slide 3: Moving Drawing Objects
Ribbon: Home  Modify  Move
Select the objects to be moved
Press [Enter] at the keyboard to finish selecting objects
Specify the base point
Specify the second point

## Slide 4: Exercises: Moving Drawing Objects
6.1.1 Moving Drawing Objects
6.1.2 Additional Practice Moving Objects
6.1.3 Moving Drawing Objects Challenge Exercise

## Slide 5: Scaling Drawing Objects
Enlarge an object with the Scale command
Reduce the size of an object with the Scale command
Scale an object using the Reference option
Objectives:

## Slide 6: Scaling Drawing Objects
Ribbon: Home  Modify  Scale
Select the objects to be scaled
Press [Enter] at the keyboard to finish selecting objects
Specify the base point
Specify the scale factor

## Slide 7: Exercises: Scaling Drawing Objects
6.2.1 Scaling Objects
6.2.2 Scaling Drawing Objects with the Reference Option
6.2.3 Scaling Drawing Objects Challenge Exercise

## Slide 8: Stretching Drawing Objects
Stretch a portion of a drawing to increase its length
Stretch a portion of a drawing to reduce its length
Objectives:

## Slide 9: Stretching Drawing Objects
Ribbon: Home  Modify  Stretch
Select the objects to be stretched with a crossing-window or crossing-polygon
Press [Enter] at the keyboard to finish selecting objects
Specify the base point
Specify the second point

## Slide 10: Exercises: Stretching Drawing Objects
6.3.1 Stretching Drawing Objects
6.3.2 Stretching Drawing Objects Challenge Exercise

## Slide 11: Rotating Drawing Objects
Rotate drawing objects
Objectives:

## Slide 12: Rotating Drawing Objects
Ribbon: Home  Modify  Rotate
Select the objects to be rotated
Press [Enter] at the keyboard to finish selecting objects
Specify the base point
Specify the rotation angle
  Positive value = counterclockwise
  Negative value = clockwise

## Slide 13: Exercises: Rotating Drawing Objects
6.4.1 Rotating Drawing Objects
6.4.2 Rotating Objects with Polar Tracking
6.4.3 Rotating Objects with the Reference Option
6.4.4 Rotating Drawing Objects Challenge Exercise

## Slide 14: Trimming Drawing Objects
Use the Trim command to remove portions of drawing objects such as lines, arcs, and polylines
Objectives:

## Slide 15: Trimming Drawing Objects
Ribbon: Home  Modify  Trim
Select the objects to be trimmed
By default all drawing objects are selected as cutting edges
At the Command line select [cuTting edges] to specify cutting edges

## Slide 16: Exercise: Trimming Drawing Objects
6.5.1 Trimming Drawing Objects

## Slide 17: Extending Drawing Objects
Use the Extend command to stretch drawing objects such as lines, arcs, and polylines, to meet other drawing objects
Quickly switch between Trim and Extend commands
Objectives:

## Slide 18: Extending Drawing Objects
Ribbon: Home  Modify  Extend
  By default, the Trim button is displayed, so it is necessary to click the drop-down arrow to access the Extend command
Select the objects to be extended
By default all drawing objects are selected as boundary edges
At the Command line select [Boundary edges] to specify boundary edges

## Slide 19: Exercises: Extending Drawing Objects
6.6.1 Extending Drawing Objects
6.6.2 Additional Practice Trimming and Extending Objects
6.6.3 Trimming and Extending Drawing Objects Challenge Exercise

## Slide 20: Creating Rounded Corners with the Fillet Command
Create rounded corners using the Fillet command
Trim/Extend lines to form a corner using the Fillet command
Simultaneously fillet all corners of a polyline
Objectives:

## Slide 21: Filleting Drawing Objects
Ribbon: Home  Modify  Fillet
Select the [Radius] option at the Command line
Specify the radius value, then press [Enter] at the keyboard
Select the first object
Select the second object

## Slide 22: Exercises: Creating Fillets
6.7.1 Filleting Drawing Objects
6.7.2 Additional Practice Filleting Drawing Objects
6.7.3 Filleting Drawing Objects Challenge Exercise

## Slide 23: Creating Angled Corners with the Chamfer Command
Create beveled corners using the Chamfer command
Trim/Extend lines to form a corner using the Chamfer command
Simultaneously chamfer all corners of a polyline
Objectives:

## Slide 24: Chamfering Drawing Objects
Ribbon: Home  Modify  Chamfer
  By default, the Fillet button is displayed, so it is necessary to click the drop-down arrow to access the Chamfer command
Select the [Distance] option at the Command line
Specify the distance values, then press [Enter] at the keyboard
Select the first object
Select the second object

## Slide 25: Exercises: Creating Chamfers
6.8.1 Chamfering Drawing Objects
6.8.2 Chamfering Drawing Objects Challenge Exercise