## Slide 1: Inquiry Tools
Measure Commands
Object Properties

## Slide 2: Measure Commands
Measure the distance between two points
Measure the radius and diameter of an arc or circle
Measure the angle between two lines
Measure the area of a region
Add and subtract regions within the area command
Determine the X,Y coordinates of a point
Objectives:

## Slide 3: Measuring the Distance Between Two Points
Ribbon: Home  Utilities  Measure  Distance

## Slide 4: Measuring the Distance Between Two Points
Select two points, using Object Snaps for accuracy
Distance and other values are shown in the Command line

## Slide 5: Measuring the Radius and Diameter of an Arc or Circle
Ribbon: Home  Utilities  Measure  Radius

## Slide 6: Measuring the Radius and Diameter of an Arc or Circle
Select an arc or circle
Radius and diameter values are shown in the Command line

## Slide 7: Measuring the Angle Between Two Lines
Ribbon: Home  Utilities  Measure  Angle

## Slide 8: Measuring the Angle Between Two Lines
Select two lines
The angle value is shown in the Command line

## Slide 9: Measuring the Area and Perimeter of a Shape
Ribbon: Home  Utilities  Measure  Area

## Slide 10: Measuring the Area and Perimeter of a Shape
Select each corner of the shape in order
Press [Enter] at the keyboard
The area and perimeter values are shown in the Command line

## Slide 11: Using the Object Option of the Area Command
After starting the Area command, select the Object option from the Command line
Select the shape
The shape must be closed, such as a circle or a closed polyline

## Slide 12: Using the Add and Subtract Options of the Area Command
Begin the Area command.
Select the [Add area] option at the Command line.
Select the [Object] option at the Command line.
Select the outer object.
Press [Enter] at the keyboard to exit the Add mode.
Select the [Subtract area] option at the Command line.
Select the [Object] option at the Command line.
Select the inner object(s).
Total area appears in the Command line.

## Slide 13: Determining the X,Y Coordinates of a Point
Ribbon: Home  Utilities fly-out  ID Point
Select a point, using Object Snaps for accuracy
X,Y coordinates are shown in the Command line

## Slide 14: Measuring with the Quick Measure Tool
Ribbon: Home  Utilities  Quick
Hover over drawing objects to display measurements

## Slide 15: Measuring with the Quick Measure Tool
Click inside of drawing objects to display area and perimeter

## Slide 16: Exercises: Measuring Tools
8.1.1 Measuring Distance, Area, and Perimeter
8.1.2 Measuring Distance, Radius, Area, and Angle
8.1.3 Measuring Angles
8.1.4 Measuring with the Quick Measure Tool
8.1.5 Measure Commands Challenge Exercise

## Slide 17: Object Properties
Describe the ByLayer option
Use the Match Properties tool to adjust the properties of an object
Use the List command to view several measurements
Use the Properties palette to view and modify several measurements
Use the Quick Select tool to create filtered selection sets
Objectives:

## Slide 18: Match Properties
Ribbon: Home  Properties  Match Properties
Select the source object
Select the destination object

## Slide 19: List Command
Ribbon: Home  Properties fly-out  List

## Slide 20: List Command
Select the object
Press [Enter] at the keyboard
Information is displayed in the AutoCAD Text Window
Information varies based upon type of object selected

## Slide 21: Properties Palette
Ribbon: View  Palettes  Properties

## Slide 22: Properties Palette
Selecting an object will display several properties
Many values can be modified

## Slide 23: Selecting Objects with Quick Select
Located in the upper-right corner of the Properties palette

## Slide 24: Selecting Objects with Quick Select
The Quick Select command will allow you to select similar objects by specifying the desired properties
  All text in a drawing
  All circles of a certain radius
  All objects on the Dimension layer

## Slide 25: Exercise: Working with Object Properties
8.2.1 Viewing and Modifying Object Properties