## Slide 1: Adding and Modifying Hatch Patterns
Adding and Modifying Hatch Patterns

## Slide 2: Adding and Modifying Hatch Patterns
Add hatch patterns using the Pick Points method
Add hatch patterns using the Select Object method
Adjust the base point of a hatch pattern
Adjust the scale of a hatch pattern
Adjust the rotation angle of a hatch pattern
Use the Match Properties tool to match an existing hatch pattern
Describe the benefit of making a hatch pattern associative
Objectives:

## Slide 3: Hatch Command
Ribbon: Home  Draw  Hatch
Three options for selecting the area to be hatched
  Draw method allows you to add hatching without the need for a physical border to help define it
  Pick points allows you to pick inside the region to be hatched
  Select objects allows you to select a polyline or other closed object

## Slide 4: Hatch Patterns
Ribbon: Hatch Creation  Pattern
There are several patterns available for different types of drawings, such as mechanical, architectural, and civil
Additional patterns are accessible by scrolling up and down, or by selecting the drop-down arrow

## Slide 5: Hatch Patterns
Hatch Angle can be adjusted to rotate the direction of the hatching lines
Hatch Scale can be adjusted to increase or decrease the size of the hatch pattern

## Slide 6: Associative Hatch Objects
Ribbon: Hatch Creation  Options  Associative
Associative hatch objects will update if the boundaries are changed
  In the example below, the inner circle was erased, and one of the corners of the box was stretched. The hatch object updated.

## Slide 7: Hatch Origin
Ribbon: Hatch Creation  Origin  Set Origin
Allows you to select an origin point for a hatch pattern

## Slide 8: Separate Hatches
Ribbon: Hatch Creation  Options  Separate Hatches
The hatch objects are now individually selectable and can be edited independently of one another

## Slide 9: Exercises: Adding and Modifying Hatch Patterns
9.1.1 Adding Hatch Patterns
9.1.2 Additional Practice Adding Hatch Patterns
9.1.3 Adding Hatch Patterns Challenge Exercise